## Slide 1: Data Types

## Slide 2: How are they stored
Stored using binary (0 or 1)
Byte - Basic unit of memory
  8 bits
All data types stored this way
  int : 32 bit (4 bytes)
  char : 8 bit (1 byte)

## Slide 3: Quick Note: Binary
Only 0 and 1 exist
Like decimal numbers grow to the left
  Binary: 1110001, Decimal: 113
  Right most bit is the zeroth order bit
  Bn nth bit
  N number of bits

## Slide 4: Integer Types
int
  32 bit
  Signed (allows negative and positive numbers)
    Range: -232 to 232-1 (-2,147,483,648 to 2,147,483,647)
  2’s complement
Flag Bit
If 0, then positive
If 1, then negative
31 bits

## Slide 5: 2’s Complement
For decimal integers
  a+(-a) = 0 ex: 19+(-19) = 0
Most modern CPUs are binary
  Not only binary
  Only positive binary
How do we add two positive numbers and get Zero?
  Multiple candidate methods
  We will only look at 2’s complement

## Slide 6: 2’s Complement (cont.)
Integer representation exists in word space
  A word is 32 bits on most machines
    64 bit is working its way out
  Use this to our advantage
    No number can be larger than 232-1
      It will just wrap back around to 0
Present two methods
  Purely binary
  Simplified decimal

## Slide 7: 2’s Complement (cont.)
Assume 8 bit word space
Some number 10010011
10010011 10010011
XOR 11111111 + 01101101
01101100 00000000
+ 00000001
01101101
01101101 is the 2’s complement of 10010011

## Slide 8: Quick Note: Hexidecimal
Values
  0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F
Each hexidecimal number rep’s a 4 bit number
0 = 0000 4 = 0100 8 = 1000 C = 1100
1 = 0001 5 = 0101 9 = 1001 D = 1101
2 = 0010 6 = 0110 A = 1010 E = 1110
3 = 0011 7 = 0111 B = 1011 F = 1111
N bit number is rep’ed by N/4 hexit number
  111111112=0xFF16 101100102 = B216

## Slide 9: 2’s Complement (cont.)
Algorithm for finding 2’s Complement
  Have binary number that populates word space
  XOR the number with 0xF…F (Binary rep of 2N-1)
  Add 0x1
This guarantees 0x0 when a number is added to its 2’s complement

## Slide 10: 2’s Complement (cont.)
Simplified Decimal method
    -B is decimal rep of 2’s complement of M
Ex: Again 8 bit word space
M = 137, 256-137 = 119, So 137 = -119
or -11910 = 100010012 , 11910 = 011101112

## Slide 11: 2’s Complement (cont.)
Range of 2’s complement
  [-2N-1,2N-1-1]
Ex: 3 bit word space
0 = 000 -4 = 100
1 = 001 -3 = 101
2 = 010 -2 = 110
3 = 011 -1 = 111

## Slide 12: Integer Types (Cont.)
unsigned int
  32 bit
  Unsigned (only allows 0 and positive numbers)
  Range: 0 to 232-1 (0 to 4,294,967,295)
No Flag Bit
32 bits

## Slide 13: Integer Types (cont.)
short
  16 bit
  Signed by default (2’s complement)
    Range: -216 to 216-1 (-32768 to 32767)
  Declare unsigned short
    Range: 0 to 216-1 (0 to 65535)
  Mainly used when dealing with sockets and ports

## Slide 14: Integer Types (cont.)
long
  64 bit
  Signed by default
    Range: -264 to 264-1 (approx -9*1018 to 9*1018)
  Declare unsigned long
    Range: 0 to 264-1 (0 to approx 1.8*1019)

## Slide 15: Floating Point Types
float
  32 bit
  Defined by IEEE 754
  Always signed
    Range: approx -8.3*1038 to 8.3*1038
Number representation
  Similar to scientific notation
  Mantissa(significand), base, exponent

## Slide 16: Floating Point Types (cont.)
double
  64 bit
  Defined by IEEE 754
  Always signed
    Range: approx -9*10308 to 9*10308
Number representation
  Similar to scientific notation
  Mantissa(significand), base, exponent

## Slide 17: Floating Point Numbers
  s mantissa
  p precision of the mantissa
  b base (radix)
  e exponent
Examples
  1.5*103, -5.32*10-8, (4.37/222)*215
1. https://en.wikipedia.org/wiki/Floating_point

## Slide 18: Floating Point Numbers (cont.)
  F floating point value
  p-1 size of the mantissa
  1 most significant bit is always 1 for non zero value
  2-n bits going to right of radix point
  2e for the exponent

## Slide 19: Single Precision (float)
Flag Bit
If 0, then positive
If 1, then negative
8 bits
Exponent
Also signed
23 bits
Mantissa
10-38 to 1038
3. https://en.wikipedia.org/wiki/IEEE_floating_point#IEEE_754-2008

## Slide 20: Double Precision (double)
Flag Bit
If 0, then positive
If 1, then negative
11 bits
Exponent
Also signed
52 bits
Mantissa
10-308 to 10308

## Slide 21: Character Type
char
  8 bit
  Defined by ASCII
    Originally 7 bits. But, Hey! Progress!
  Get all values from ASCII tables
    Remember to put a 0 in front
      Traditional ASCII

## Slide 22: ASCII Table
4. https://en.wikipedia.org/wiki/ASCII

## Slide 23: Reading ASCII Table
Bit format
  Ex: character a

## Slide 24: Further Reading
D. Knuth, The Art of Computer Programming Vol. 2, Addison-Wesley, 1997
http://www.cse.msu.edu/~cse320/Documents/FloatingPoint.pdf
IEEE 754-2008 revision